## Slide 1
NEURAL NETWORKS | ECE 542
Neural Sequence Modeling for Advanced Microarchitectural Branch Prediction
Baseline ML Models Implementation
· Shreeya Ranwadkar · Advika Metre · Prajna Hassan Umesh

## Slide 2
MOTIVATION & PROBLEM STATEMENT
Why Does Branch Prediction Matter?
15–20%
of instructions
are branches
~30%
of total CPU cycles
wasted on mispredictions
15+ cycles
penalty per
mispredicted branch
Problem Statement
Modern CPUs rely on branch predictors to speculatively execute instructions. Incorrect predictions stall the pipeline and degrade performance. Traditional predictors (bimodal, gshare) use fixed heuristics. We ask: can machine learning models learn branch behavior from historical traces and outperform a trivial always-predict baseline?

## Slide 3
BACKGROUND
How Branch Prediction Works
Fetch
PC address
Predict
Taken / Not Taken?
Execute
Evaluate branch
Commit/
Flush
Correct or penalize
Taken (label = 1)
Branch jumps to target address
Loop back-edges, if-conditions
Pipeline must flush if wrong
Not-Taken (label = 0)
Branch falls through sequentially
Straight-line code continues
~51% of gcc trace branches

## Slide 4
PRIOR WORK
Prior Work by Team Members
Branch Predictor Simulator
Modeled Bimodal, Gshare, and Hybrid branch predictors with 2-bit Smith counters
Simulated over 0.2 million branch traces to evaluate predictor behavior
Analyzed prediction accuracy by adjusting simulator parameters (history bits, table sizes)
This prior work established the hardware context for this project: understanding how classical predictors like Bimodal and Gshare work — using fixed-width counters and history registers — directly informed the feature design (PC history + outcome history) used in our ML models.

## Slide 5
DATASET
gcc_trace — Prior Coursework Dataset
Source
Branch trace dataset from prior coursework (ECE 563)
Generated as part of a branch predictor simulation project
Entry Format & Encoding
Each entry contains: Program Counter (PC) address + branch outcome (t = taken, n = not taken)
Data converted to binary: taken → 1, not taken → 0
Sequential trace preserves execution order
Used to model real program control-flow behavior
500,000
Total Branches
First 500k used (temporal order)
80 / 20%
Train / Test Split
No shuffle — preserves time order
57.3%
Taken (label=1)
Majority class in training set
42.7%
Not-Taken (label=0)
Minority class in training set

## Slide 6
BASELINE & METRICS
Trivial Baseline + Evaluation Metrics
Trivial Baseline
Always predicts the majority class from training. Train set has 57.3% Taken — so trivial predictor always predicts Taken.
Accuracy: 51.48% · Misprediction: 48.52%
This is the floor — any useful ML model must beat this. It represents zero learning: no history, no patterns, pure majority vote.
Evaluation Metrics
Misprediction Rate
(1 − Acc) × 100. Primary metric. Maps to CPU pipeline stalls.
Accuracy
Fraction of branches correctly predicted overall.
Precision
TP / (TP+FP). Of predicted Taken, how many were actually Taken?
Recall
TP / (TP+FN). Of actual Taken branches, how many did we catch?
F1-Score
Harmonic mean of Precision and Recall. Balances both.
Confusion Matrix
TN / FP / FN / TP breakdown — reveals bias toward Taken class.
Parameter Footprint
# weights (LR) or tree nodes (DT/RF). Hardware budget proxy.
Training Time
Wall-clock seconds. Reflects model complexity at scale.

## Slide 7
BASELINE MODELS
Three Classical ML Approaches
Logistic Regression
65 parameters
Config: solver=saga, C=1.0, max_iter=300
Learns a linear decision boundary in the 64-dimensional feature space. Assigns a probability to the 'Taken' class using a sigmoid function.
✓ Extremely lightweight — closest to hardware-deployable
✗ Cannot model non-linear branch patterns
Decision Tree
5,119 nodes
Config: max_depth=15
Recursively splits feature space on thresholds. Each path from root to leaf is a prediction rule based on PC history and branch outcomes.
✓ Interpretable — rules can be inspected
✗ Prone to overfitting; single tree is brittle
Random Forest
666,102 nodes
Config: 100 trees, max_depth=15
Ensemble of 100 decision trees. Each tree sees a random subset of features. Final prediction is a majority vote across all trees.
✓ Best accuracy — captures complex patterns
✗ Very large parameter footprint; slow (74s)

## Slide 8
OUTPUT

## Slide 9
RESULTS
Performance Summary
Model | Accuracy | Mispred. Rate | # Params | Train Time
Trivial Baseline | 51.48% | 48.52% | — | —
Logistic Regression | 57.80% | 42.20% | 65 | 24.2s
Decision Tree | 65.60% | 34.40% | 5,119 | 20.9s
Random Forest ★ | 67.85% | 32.15% | 666,102 | 55.7s
Classification Reports (from actual run)
Logistic Regression
Not-Taken P:0.58 R:0.50 F1:0.53
Taken P:0.58 R:0.65 F1:0.61
TN=24,117 FP=24,403
FN=17,798 TP=33,676
Decision Tree
Not-Taken P:0.68 R:0.54 F1:0.60
Taken P:0.64 R:0.76 F1:0.70
TN=26,221 FP=22,299
FN=12,100 TP=39,374
Random Forest
Not-Taken P:0.75 R:0.50 F1:0.60
Taken P:0.64 R:0.85 F1:0.73
TN=24,280 FP=24,240
FN=7,909 TP=43,565

## Slide 10
NEXT STEPS
Neural Network Extensions
LSTM
Long Short-Term Memory
Designed for sequential data — ideal for branch histories
Remembers long-range correlations across hundreds of branches
Hidden state acts as a learned branch history register
Expected: significantly lower misprediction rate vs. RF
MLP
Multi-Layer Perceptron
Fully connected deep network on the same 64-feature input
Multiple hidden layers capture non-linear branch interactions
Faster to train than LSTM; good accuracy-cost tradeoff
Can be quantized for approximate hardware deployment

## Slide 11
REFERENCES
References
[1] gcc_trace Dataset — Branch trace from prior coursework (ECE 563), NC State ECE.
Generated as part of a branch predictor simulation project. Used with permission. [2] Jiménez, D. A., & Lin, C. (2001). Dynamic branch prediction with perceptrons. Proceedings HPCA Seventh International Symposium on High-Performance Computer Architecture. [3] Elbtity, M. B. E., et al. (2023). An LSTM-based Branch Predictor for Modern Microprocessors. IEEE International Symposium on Circuits and Systems (ISCAS)